## Slide 1: Some thoughts on IoT
Geoff Huston
Chief Scientist, APNIC

## Slide 2: Technology
Technology
Does technology change society, or do we develop and adopt technology to address society’s changes?
When Meng Tian invented the camel hair paintbrush in 250 BCE he did not invent calligraphy. He responded to a need in ancient Chinese society for more and higher quality written documents that could be produced faster
Does technology change society, or do we develop and adopt technology to address society’s changes?
When Meng Tian invented the camel hair paintbrush in 250 BCE he did not invent calligraphy. He responded to a need in ancient Chinese society for more and higher quality written documents that could be produced faster

## Slide 3
The most profound technologies are those that disappear. They weave themselves into the fabric of everyday life until they are indistinguishable from it...
- Mark Weiser 1991
Technology

## Slide 4
So how should we look at the Internet of Things?
Is this merely a temporary consumer fad, destined to be replaced by the next cool technology item?
Or is this an instance of a profound technology change that answers a basic need in our society that will bed down to be a part of our everyday life for many years to come?

## Slide 5
To try and answer this, lets try and put this question into some broader context of the evolution the computer and communications enterprise

## Slide 6: Computers were esoteric high frontier research projects
1946 – Eniac – a numeric calculator

## Slide 7: Then they became a “must have” business tool
1964: IBM 360
1964 IBM 360 – commercial computing

## Slide 8: The Computing Evolutionary Path
Extravagant statements of techno power
1976 CRAY-1 – “super” computing

## Slide 9: The Computing Evolutionary Path
1976: Apple I
But there was also the hobbyist market
1976 – Apple-1 “personal” computing

## Slide 10
Consumer computers as a statement of design style
1984 – Mac

## Slide 11
From Style to Mass Marketed Luxury Item
2007 – Apple’s iPhone

## Slide 13
With desktop devices the Internet of computers was a dedicated activity
dedicated chair
lighting
wired bandwidth
large view screens
privacy
dedicated worktop
reliable power

## Slide 14
The Internet is now anywhere and everywhere
Its trivial, commonplace and blends into all our activities
radio connectivity
battery power
hand sized
Thumb
operated

## Slide 15
As dedicated “things” are replacing it
Maybe its about the demise of the “traditional” computer

## Slide 16
Connecting “things” to the Internet is nothing new
Simon Hackett’s Internet Remote Radio of 1990

## Slide 17
John Romkey’s Internet Toaster – Let them eat Toast!
Connecting “things” to the Internet is nothing new

## Slide 18: This new IoT is just the old IoT
The use of microprocessors to undertake simple tasks is about as old as the Intel 4004 and the Zylogics Z80 processor chips

## Slide 19: This new IoT is just the old IoT (with new lipstick!)
This new IoT is just the old IoT (with new lipstick!)
And we are already living in a processing-dense world
  A modern car has around 150 – 200 microprocessor-controlled systems, from the windscreen wipers, to the entry system, to engine control and all things in between
  Many / most consumer appliances have all turned to microprocessor control
  Industrial processes, logistics and inventory control, environmental monitoring all use various forms of embedded processing
So why is IoT a hot topic today?
And we are already living in a processing-dense world
  A modern car has around 150 – 200 microprocessor-controlled systems, from the windscreen wipers, to the entry system, to engine control and all things in between
  Many / most consumer appliances have all turned to microprocessor control
  Industrial processes, logistics and inventory control, environmental monitoring all use various forms of embedded processing
So why is IoT a hot topic today?

## Slide 20: The Hype
Gartner Predictions
CES shows
Home Apps
Car Apps

## Slide 21: IoT is …?
It is a generic term that encompasses a huge variety of application that have little in common other than a propensity to operate in an unmanaged environment
Its hard to talk about the IoT in anything other than highly generic terms

## Slide 22: Why now?
Low power, high capability silicon now dominates chip fabrication plants
  Saturation of the smart device market
  Full stream silicon production volumes requires some form of consumption model
Radio Technology: RFID, Bluetooth, WiFi, LTE
  Improvements in AD convertors is providing range and bandwidth to radio systems
  Protocol development provides ”seamless” connectivity
  i.e. Passports and Clothing Tags, Apple earbuds, Home controllers and similar
Actors seeking new markets
  5G for SIMs and wide area mobility
  Smart phone platform providers seeking to enter the car, home and work environments
  Industrial and process automation seeking to expand market reach

## Slide 23: Why now?
Because we have saturated our traditional markets for technology and the production capacity is being redirected to new opportunities
  PC sales volumes plummeting
  Smartphone sales are now peaking
  The computer technology industry is seeking to use its existing capability to provide new product to high volume markets
  Which means looking at low unit margin very high volume opportunities by adding ”smart” network centric interfaces and controllers to existing devices and functions

## Slide 24: The opportunities
“smart” lighting - e.g. Philips
“smart” home appliances and networks - e.g. Miele
“smart” power management
”smart” labels for retail
“smart” traffic control
“smart” image analysis
“smart” video surveillence
Almost anything else that uses the word “smart”

## Slide 25: The Variety of Life
It’s a set of discrete applications that have highly divergent requirements:
  Radius of connectivity varies from mm to kilometers
  Bandwidth varies from bits to gigabits per second
  Data volumes vary from bytes to petabytes
  Connectivity models may be push or pull
  Connectivity may be ad-hoc relays to dedicated wired
  Transactions may be unicast, multicast or anycast in nature
  Applications include sensing and reporting, command and control, adaptation and interfacing
There is little that these environments have in common, except maybe a common underlying gene pool!
IoT

## Slide 26: The IoT Gene Pool
Unix
  Its small, its ubiquitous, its well understood, its cheap, its open source without onerous IPR constraints, it has a massive set of application libraries
  Customised micro kernels are risky, expensive and rarely necessary
IP
  Its small, its ubiquitous, it scales, its well understood, its cheap, its open source without onerous IPR constraints, and everyone speaks it!
  But which IP?

## Slide 27: IPv4 and IoT
The “conservative” option for IP in this environment
  Ubiquitous support across the entire deployed Internet
  Well understood protocol behaviour
  Widely available APIs
  Of course it should also be useful to factor in NATs in IPv4:
  Push model where the “thing” pushes data to a rendezvous point rather than a constant pollable model of “pull” access
  “pull” and “feeder” models work behind NATs using relays and/or ALGs split the primary feed from the propagation of the data

## Slide 28: IPv6 and IoT
It’s the “killer app” for IPv6
But the numbers suggest otherwise:
  7B connected “devices” on today’s IPv4 Internet, plus a further 7B conventional PC and smart devices
  2.8B announced IPv4 addresses
  1.3B “used” IPv4 addresses
  We can probably push this model harder!

## Slide 29: “Thing” Behaviour
Pull:
Device is always connected and interrogated by external agents
  A model of polling or feed subscription where the device maintains information that can be polled by an external agent
  This requires an public IP address + Port
  It also requires a highly robust core implementation that is resistant to attack
  It also requires some considerable thought on the authorization model
    Device is configured to authorize users and/or
    Device uses a third party auth server
  Commonly seen in web cams and other continuous monitoring applications (though it’s not necessarily required)

## Slide 30: Pull vs Push
Push:
Intermittedly connected and interrogated via external agents
  Device pushes data to some data collection agent
  Limited connection requirement
  This behaviour NAT ”friendly” as the device is the client and the collection point is the server
  External access via the data collection agent, not the device
  Does not require dedicated addressing outside of the local context
  This limited access model facilitates defensive measures, including encrypted communications to the device’s agents and preventing all third party connections
  And such devices probably should be behind a NAT in any case! (e.g. cameras)

## Slide 31: Security

## Slide 32: Seen at NANOG 69…

## Slide 33: Security
Interesting ...
“At last count I have about 43 devices on my LAN, with less than a third running an OS that I can actually interact with. The rest are embedded systems that get updated (hah!) by the vendors at their whim. Easily two-thirds would 'phone home' to somewhere at various times. About 7 have external access without explicitly setting port-forwarding.
Of course, my router monitors and reports on all outbound traffic - but do I actively look at it? I should. But I don’t. And of course everything we value on our LAN we protect and encrypt end-to-end and at-rest as the LAN is actually occupied by foreign devices with unknown network capability... sure we encrypt absolutely everything...”

## Slide 34: An Internet of Stupid Things
We keep on seeing the same stupidity again and again:
Devices with the telnet port open
Devices with open DNS resolvers on the WAN side
Devices with open NTP / SNMP / chargen etc
Devices with the same preset root password
Devices using vulnerable libraries that are susceptible to root kit exploitation
Insanely

## Slide 35: The Internet of Stupid Things
How do you perform field upgrades of otherwise neglected and unmanaged devices
What’s the economics of incenting field upgrades from the manufacturer?
Who is responsible for broken “things”?

## Slide 36: The Internet of Stupid Things
Is this stupidity even avoidable?
  The bleak picture is maybe not!
  In a price sensitive market where system robustness and quality is largely intangible where is the motive to maintain high quality code?
  How can a consumer tell the difference in the quality of the software, in term of its robustness and security of operation?
  high clockspeed industry + commodity components + low margin = market failure for IoT Security

## Slide 37: Privacy

## Slide 38: Privacy

## Slide 39: Some things you can count on…
The volumes are already huge, and they’re growing
  “Things” already outnumber everything else on the Internet
Security is an unachievable word!
Privacy is now an historical concept
Digital pollution is pervasive and we now have an internet that is a largely chaotic and hostile environment

## Slide 40: And some things we can’t tell
Will we standardize this area or will it be a diverse set of mutually incompatible devices?
Will the market consolidate to be dominated by a small number of providers and their pseudo-open proprietary architectures?
When will the IoT embrace IPv6?
Will the IoT market ever discriminate on quality and rebustness?
How do we manage the risk of coercion of these devices?

## Slide 41: And some things we can’t tell
How bad can it get?

## Slide 42: It’s a tough problem…
"The market can't fix this because neither the buyer nor the seller cares.
The owners of the webcams and DVRs used in the denial-of-service attacks don't care. Their devices were cheap to buy, they still work, and they don't know any of the victims of the attacks.
The sellers of those devices don't care: They're now selling newer and better models, and the original buyers only cared about price and features.
There is no market solution, because the insecurity is what economists call an externality: It's an effect of the purchasing decision that affects other people. Think of it kind of like invisible pollution."
https://www.schneier.com/blog/archives/2017/02/security_and_th.html

## Slide 44: Thanks!